## Slide 1
FACULTY OF ENGINEERING AND TECHNOLOGY
ELECTRICAL AND COMPUTER ENGINEERING DEPARTMENT
ADVANCED COMPUTER ARCHITECTURE
ENCS5331
Name: Kareem Hamza ID: 1220708
Name: Noor Battat ID: 1210075
Name: Anas Sarabtta ID: 1200242
DR. AYMAN HROUB
PROJECT PRESENTATION :
NM-RAG: A NEAR-MEMORY COMPUTING ACCELERATOR FOR RETRIEVAL-AUGMENTED GENERATION SYSTEMS

## Slide 2
  Introduction
  Problem & Motivation
  Contributions
  Related Work & Gap
  Proposed Solution (Architecture + Quantization + Pipeline)
  Experimental Results
  Conclusion
Outline

## Slide 3
  What is RAG? It retrieves relevant passages from a vector database, then the LLM generates an answer using that context.
  Why it matters: user experience depends on TTFT, which includes retrieval latency + prefill.
  This work’s focus: accelerate the retrieval stage (the memory bottleneck).
Introduction

## Slide 4
Problem Statement and Motivation
  RAG retrieval is the bottleneck: for each user query, the system must score a large embedding database to fetch the top-K relevant passages.
  Memory bandwidth dominates: similarity search needs many embedding reads, so performance is limited by data movement more than compute.
  Existing options have drawbacks:
    ANN methods speed up search but can reduce recall/quality and may add unpredictable behavior.
    GPU acceleration can help compute, but PCIe transfers + limited GPU memory + power cost are major constraints.
  Motivation: we need a retrieval engine that is fast, energy-efficient, and scalable to large corpora—without sacrificing too much retrieval quality.
  Goal: Sub-millisecond top-K retrieval for RAG by reducing data movement (compression) and moving compute near memory.

## Slide 5
  Near-memory retrieval architecture: a specialized design for RAG retrieval using a host interface + many Near-Memory Processing Units (NMPUs) + a hardware Top-K aggregation unit.
  Quality–performance co-design via quantized retrieval: PCA-based compression (384D → 128D) with int8 vectors to reduce bandwidth/data movement while keeping usable recall.
  Rigorous evaluation methodology: a cycle-accurate performance model that includes realistic bandwidth efficiency, synchronization, and system overheads, plus comparison vs CPU/GPU/ANN baselines.
Contributions

## Slide 6
Related Work Summary and Literature Gap
  ANN/ANNS retrieval (HNSW, IVF-PQ): improves speed, but can degrade recall and causes irregular memory access / unpredictable latency (pointer chasing).
  GPU retrieval (e.g., FAISS-GPU): parallelizes dot products, but faces PCIe transfer overhead, limited GPU memory (caps corpus size), and high power (80–300W).
  Generation-side compression (REFRAG / chunk compression): reduces LLM prefill/TTFT, but does not reduce retrieval latency (retrieval must finish first).
  Literature gap: existing solutions do not eliminate the fundamental memory-bandwidth bottleneck of exact vector search for retrieval at scale.
  NM-RAG fills this gap by moving similarity compute near memory and reducing data movement via 128D int8 quantization.

## Slide 7
Proposed Solution
  Goal: accelerate RAG retrieval by moving similarity search near memory and minimizing data movement.
  Host Interface (CXL 2.0): cache-coherent access + command submission from CPU.
  64 Near-Memory Processing Units (NMPUs): parallel compute units colocated with HBM3.
  Hardware Top-K Selection Unit: merges local top-K lists into final results efficiently.
Fig: NM-RAG architecture (CXL 2.0 host interface, 64 NMPUs + HBM3, hardware Top-K).

## Slide 8
Hardware Design (NMPU + Memory Subsystem)
  NMPU core: 256-bit SIMD for 8-bit dot products (32 elements/cycle) + 64KB scratchpad + controller to a dedicated HBM bank.
  Dot-product efficiency: 128-D vector dot product completes in 4 cycles with this SIMD width.
  HBM3 design: 900 GB/s aggregate, 14 GB/s per NMPU, partitioned banks to avoid contention and enable true parallelism.
Fig: NMPU internals (SIMD vector engine + 64KB buffer + local HBM access).

## Slide 9
Algorithm + Query Flow (Quantization + Pipeline)
(A) Vector Quantization Strategy (reduce bandwidth)
  Apply PCA + whitening offline; compress embeddings 384D → 128D (3×).
  Quantize to int8 range [-127,127] and pack for memory efficiency (128 bytes/document vs 1536 bytes originally).
  Chosen operating point: 128D balances quality and speed (75.6% recall) vs more/less aggressive dims.
Fig: Query processing pipeline + per-stage latency breakdown
(B) Query Processing Pipeline (how it runs)
  Host: encode query → PCA quantize → submit via CXL.
  NMPUs: broadcast query → parallel dot products → local top-K.
  Top-K unit: merge 64 local lists → return global top-K results.

## Slide 10
Experimental Results
  NM-RAG latency: 0.48 ms/query (CPU 7.00 ms, GPU 6.78 ms, ANN 1.59 ms)
  Speedup: 14.6× vs CPU, 4.4× vs ANN
  Energy/query: 0.0014 J → 125× lower vs CPU, 380× vs GPU, 23× vs ANN
  Quality: Recall@100 = 75.6% (ANN 29.8%), MRR = 1.0, nDCG@100 = 80.99%
  Throughput: 2,091 QPS (single-query)
TABLE: PERFORMANCE COMPARISON OF RAG ACCELERATION METHODS

## Slide 11
Latency Results
  0.48 ms average query latency (14.6× faster than CPU baseline)
  CPU spends most time on memory access (fetching 150 MB for 100K docs)
  Key drivers of speedup:
    HBM3 bandwidth (900 GB/s) vs DDR5 (~100 GB/s)
    64 NMPUs parallelism (partitioned processing)
    3× compression (384D→128D) reduces transfer to 12.5 MB and enables int8 SIMD
  Note: 91% of NM-RAG latency is modeled as system overhead → optimization headroom
Fig: Retrieval Latency Comparison

## Slide 12
Energy Efficiency
  Energy/query = 0.0014 J
  Energy reduction: 125× vs CPU, 380× vs GPU, 23× vs ANN
  Why energy drops:
    No DRAM/PCIe transfers (only internal HBM access, much lower pJ/bit)
    Lower power envelope (3W vs 25W CPU / 80W GPU)
    Shorter execution time (0.48 ms vs 7 ms)
Fig: Energy Consumption Comparison

## Slide 13
Retrieval Quality
  Recall@100 = 75.6% (ANN 29.8%) → 2.5× better recall
  MRR = 1.0 (most relevant doc ranks first)
  nDCG@100 = 80.99% (strong ranking quality)
  Important interpretation: quality loss vs exact (100%) comes from PCA quantization, not hardware
  Top-K stability: Top-10 recall ~99.8%; degradation mainly in mid/low relevance results
Fig: Retrieval Quality Comparison — Recall@100

## Slide 14
Scalability + Throughput
Speedup increases with dataset size (memory bottleneck grows in CPU/GPU):
  10K docs: 8.2×
  100K docs: 14.6× (evaluated)
  1M docs: 22.3× (projected)
  10M docs: 35.7× (projected)
Throughput scaling via batching/pipelining:
  1 query: 0.48 ms → 2,091 QPS
  4-query batch: 0.52 ms total → 7,692 QPS (3.7×)
  16-query batch: 0.68 ms total → 23,529 QPS (11.2×)
Fig: Speedup vs CPU Baseline across corpus sizes

## Slide 15
Latency vs Quality Tradeoff + Credibility vs Prior Work
  Tradeoff view: NM-RAG is much faster than exact CPU/GPU while keeping much higher quality than ANN
  Key insight: hardware acceleration + moderate compression gives better balance than “approximate in full space”
  Positioning vs published near-memory systems (Table II):
    NM-RAG: 0.48 ms, 14.6×, (simulation)
    IKS / MemANNS / NDSEARCH are in the same credible range but target different points
Fig: Latency vs Quality tradeoff scatter plot
TABLE: COMPARISON WITH PUBLISHED NEAR-MEMORY SYSTEMS

## Slide 16
Conclusion
  Main takeaway: NM-RAG shows that moving retrieval compute near memory and reducing data movement can deliver sub-millisecond retrieval with major energy savings.
  Best design point: 128-D int8 (from 384-D) is the strongest balance between speed/bandwidth reduction and retrieval quality.
  Limitations: retrieval quality is lower than exact search due to PCA/quantization, and the evaluation is based on a cycle-accurate simulation model (not a hardware prototype).
  Future work: reduce system overheads and validate with a production/prototype implementation, and explore hybrid strategies (e.g., multi-stage retrieval or hybrid precision) to improve recall further.